## Slide 1: IoT GATEWAYS AND SECURITY
IoT GATEWAYS AND SECURITY Connectivity is one of the important challenges in designing the IoT network.
The diversity of sensors makes it very difficult to provide IP connectivity.
It is important that non-IP devices too have a mechanism to connect with IoT.
There are different ways nodes connected.
Gateways effectively mitigate the great variety and diversity of devices by consolidating data from disparate sources and interfaces and bridging them to the Internet.
The result is that individual nodes do not need to bear the complexity or cost of a high-speed Internet interface in order to be connected.

## Slide 2
The network nodes connect to the IoT via a gateway. The nodes themselves are not IP-based and thus cannot directly connect to the Internet/WAN.
Rather, they use either wired or wireless PAN technology to connect to the gateway with a less expensive and less complex mode of connectivity. The gateway maintains an IoT agent for each node that manages all data to and from nodes. In this case, application intelligence can also be located in the gateway.
The nodes can also connect directly to the Internet using a WAN connection such as Wi-Fi or Ethernet. The gateway serves primarily as a router; in fact, it can be simply a router when nodes have their own IoT agent and autonomously manage themselves.
Alternatively, the nodes can connect directly to the Internet using a PAN connection such as 6LoWPAN. In this case, the gateway serves as a translation point between the PAN and WAN.
IoT GATEWAYS AND SECURITY

## Slide 3
Many IoT applications handle potentially sensitive data.
Data collected from location services, need to be protected from hacking.
Similarly, medical devices need to maintain the privacy of individuals. In the context of the IoT gateway architecture, the security processing and mechanisms can be offloaded from nodes to the gateway to ensure proper authentication, protecting exchanges of data, and safeguarding intellectual property.
This enables IoT nodes to implement greater security than could be economically implemented in individual end points.
IoT GATEWAYS AND SECURITY