## Slide 1: Security and Privacy
Many IoT applications handle potentially sensitive data.
Data collected from location services, need to be protected from hacking.
Similarly, medical devices need to maintain the privacy of individuals. In the context of the IoT gateway architecture, the security processing and mechanisms can be offloaded from nodes to the gateway to ensure proper authentication, protecting exchanges of data, and safeguarding intellectual property.
This enables IoT nodes to implement greater security than could be economically implemented in individual end points.

## Slide 2: IoT ROUTING ATTACKS
Some well known routing attacks on IoT are as follows:
https://www.youtube.com/watch?v=hCFXTOWvh9M
Selective-forwarding attacks
Sinkhole attacks
Hello flood attacks
Wormhole attacks
Clone Id and Sybil attacks

## Slide 3
Selective-forwarding attacks :
A malicious node within the network selectively chooses which data packets to forward and which to drop or discard, with the intent of disrupting network operations, causing congestion, or compromising data integrity.
This attack is primarily targeted to interrupt routing paths.
For example, an attacker could forward all RPL ( Routing protocol for Low-Power and Lossy Network) control messages and drop the rest of the traffic. This attack has severe consequences when coupled with other attacks such as sinkhole attacks.
One of the solutions to guard against selective forwarding attacks is to create disjoint paths between the source and the destination nodes. Disjoint paths between source and destination nodes refer to multiple routes or paths in a network where no common links or nodes are shared between them.
Another effective counter measure against selective-forwarding attacks is to make sure the attacker cannot distinguish between different types of traffic, thus forcing the attacker to either forward all traffic or none.
The Routing Protocol for Low-Power and Lossy Networks (RPL) is a novel routing protocol standardized for 6LoWPAN networks.
IoT ROUTING ATTACKS

## Slide 4: IoT ROUTING ATTACKS
Sinkhole attacks : An attacker diverts network traffic to a malicious or unauthorized destination
SINKHOLE ATTACK is an insider attack were an intruder compromise a node inside the network and launches an attack.
Then the compromise node try to attract all the traffic from neighbour nodes based on the routing metric that used in routing protocol.
In sinkhole attacks, a malicious node advertises a fraudulent routing path with a seemingly favorable route metric. This attracts many nearby nodes to route traffic through it.
An intrusion detection system could be hosted in the 6LBR(6LoWPAN Border Routers) can detect sinkhole attacks.
(6LoWPAN: 6LoWPAN (IPv6 over Low-Power Wireless Personal Area Networks) is primarily designed for low-power, resource-constrained devices in IoT and wireless sensor networks. It is used for applications where devices need to communicate over short distances and have limited processing power, memory, and energy resources)

## Slide 5: IoT ROUTING ATTACKS
The hello-flood attack:
A "Hello Flood" attack is a type of distributed denial-of-service (DDoS) attack that targets network protocols, particularly those that involve handshake or negotiation processes.
The HELLO message refers to the initial message a node sends when joining a network.
By broadcasting a HELLO message with strong signal power and a favorable routing metric, an attacker can introduce himself as a neighbor to many nodes, possibly the entire network.
A simple solution to this attack is for each HELLO message the link is checked to be bidirectional.

## Slide 6: IoT ROUTING ATTACKS
A wormhole is an out-of-band connection(out-of-band means outside of the system knowledge), between two nodes using wired or wireless links.
In the wormhole attack, an attacker records packets at one location in the network, tunnels them to another location, and retransmits them into the network.
Wormholes can be used to forward packets faster than via normal paths
A wormhole created by an attacker and combined with another attacks, such as sinkhole, is a serious security threat.
One approach is to use separate link-layer keys for different segments of the network.
This can counteract the wormhole attack, as no communication will be possible between nodes in two separate segments.
To overcome a wormhole attack, the idea is to use geographic information as part of the network's security measures.

## Slide 7: IoT ROUTING ATTACKS
clone-ID attack: In a clone ID attack, an attacker copies the identities of a valid node onto another physical node.
In a Clone-ID attack, the attacker replicates the identity, device credentials, or authentication information of legitimate IoT devices. This allows the cloned devices to impersonate the genuine devices. Clone-ID attacks can disrupt the normal functioning of the IoT network by introducing fraudulent or conflicting devices.
This can be used in order to gain access to a larger part of the network.
In a Sybil attack, which is similar to a clone ID attack, an attacker uses several logical entities on the same physical node.
Sybil attacks can be used to take control over large parts of a network without deploying physical nodes.
By keeping track of the number of instances of each identity it is possible to detect cloned identities.
It would also be possible to detect cloned identities by knowing the geographical location of the nodes, as no identity should be able to be at several places at the same time.