## Slide 1: IoT SECURITY OVERVIEW
This section presents necessary background on the IoT control protocols such as
ZigBee, IPv6 over Low-power WPAN (6LoWPAN), Constrained RESTful Environments (CoRE), CoAP, and security protocols such as IKEv2/IPSec, TLS/SSL, Datagram Transport Layer Security (DTLS), Host Identity Protocol (HIP), Protocol for Carrying Authentication for Network Access (PANA), and Extensible Authentication Protocol (EAP).
It also discusses the key concepts on IoT security that includes identity management, authentication, authorization, privacy, trust, and governance for IoT networks

## Slide 2: IoT SECURITY OVERVIEW
IoT PROTOCOLS
NETWORK AND TRANSPORT LAYER CHALLENGE
IoT GATEWAYS AND SECURITY
IoT ROUTING ATTACKS
BOOTSTRAPPING AND AUTHENTICATION
AUTHORIZATION MECHANISMS

## Slide 3
A typical IoT layer for a Bluetooth Smart enabled device protocol stack is shown
IoT SECURITY OVERVIEW

## Slide 4
IoT PROTOCOLS
IPv6 significantly expands the number of available IP addresses for use by providing 2128 addresses.
This means that, if necessary, every device can have its own unique IPv6 address.
Standards such as 6LoWPAN have made it possible to integrate sensors in a IoT network.
6LoWPAN enables sensors to talk to IP Protocols natively.
Furthermore, new application layer protocols such as CoAP and Message Queue Telemetry Transport (MQTT) ensure optimal use of bandwidth and resources of constrained IoT devices.
Bluetooth Smart is an open standard that is specifically designed for the needs of battery powered sensors and wearable.
IoT SECURITY OVERVIEW

## Slide 5
NETWORK AND TRANSPORT LAYER CHALLENGES
The IPSec uses the concept of a Security Association (SA), defined as the set of algorithms and parameters (such as keys) used to encrypt and authenticate a particular flow in one direction.
To establish a SA, IPSec can be preconfigured (specifying a pre shared key, hash function, and encryption algorithm) or can be dynamically negotiated by the IPSec Internet Key Exchange (IKE) protocol.
The IKE protocol uses asymmetric cryptography, which is computationally heavy for resource-constrained devices. To address this issue, IKE extensions using lighter algorithms should be used.
CoAP proposes to use the DTLS protocol to provide end-to-end security in IoT systems. The DTLS protocol provides a security service similar to TLS, but on top of UDP
DTLS is a heavy weight protocol and its headers are too long to fit in a single IEEE 802.15.4 MTU. 6LoWPAN provides header compression mechanisms to reduce the size of upper layer headers.
IoT SECURITY OVERVIEW

## Slide 6
BOOTSTRAPPING AND AUTHENTICATION
Bootstrapping and authentication controls the network entry of nodes.
Authentication is highly relevant to IoT and is likely to be the first operation carried out by a node when it joins a new network.
It is performed with a (generally remote) authentication server using a network access protocol such as the PANA
Upon successful authentication, higher layer security associations could also be established and launched between the newly authenticated endpoint and the access control agent in the associated network.
IoT SECURITY OVERVIEW

## Slide 7
AUTHORIZATION MECHANISMS
The OAuth (Open Authorization) protocol has been defined to solve the problem of allowing authorized third parties to access personal user data.
OAuth2.0 is an authorization framework that allows a third party to access a resource owned by a resource owner without giving unencrypted credentials to the third party
The OAuth 2.0 protocol defines the following four roles.
1.Resource Owner 2. Resource Server (Service Provider, SP)
3. Client (Service Consumer, SC) 4. Authorization Server
For example, assume that a health care sensor or mobile app wants to access a Facebook profile to post status updates.
There is no need to provide the Facebook credentials to the app; instead, the user logs into Facebook, and as a result the app is authorized to use Facebook on the user’s behalf.
The user can also revoke this authorization any time by deleting the privilege setting
IoT SECURITY OVERVIEW