## Slide 1: ADDRESSING RELIABILITY

## Slide 2: ADDRESSING RELIABILITY-fault prevention
Reliable system take the approach of either fault prevention or fault tolerance to ensure reliability and availability
To prevent a failure, proactive actions are taken to stop the possible failure of a running system.
Prevention many a times becomes quite difficult, as there are many unanticipated external as well as transient faults due to reasons often beyond the realm of our control

## Slide 3: ADDRESSING RELIABILITY- fault tolerance
Definition: Fault-tolerance on the other hand implies that the system is able to operate in the presence of faults.
Fault-tolerance is achieved mainly through nullifying the impact of an error (also known as error masking), error detection, and recovery. The system can nullify the impact of an error mostly through employing a set of redundant components.

## Slide 4: NULLIFYING IMPACT OF FAULT (technique for addressing reliability)
A common approach for a traditional high-availability cluster is to reduce the impact of a fault as much as possible by eliminating the single point of failure (SPOF) both at the hardware and at the software level.
A common technique for this is to increase redundancy at various levels such as the infrastructure, the network, and in the software.
A simplified model to calculate the reliability of a system with redundancy having N components (a hardware or a software), of which it is sufficient to have K components operational, can be expressed
as where R denotes the reliability of a component.

## Slide 5
Redundancy in Service Platform Design
Redundancy in M2M Topology
Graceful Degradation
NULLIFYING IMPACT OF FAULT

## Slide 6: Redundancy in Service Platform Design
A good design to build a robust IoT service platform is to introduce a set of loosely coupled components so that the failure of one component does not bring the entire platform down.
Depending on the application scenario, one can then deploy multiple copies of the critical components.
Many times database systems become an integral part of the platform where the data from different communicating objects are collected for analysis. In such a case, the database system can also be a SPOF.
Depending on the nature of the application one can adopt the following redundancy strategies:
1. Load balancing across multiple databases: The load of the incoming data can be shared across multiple databases
2. Data replication: Multiple copies of data can be stored in the vast storage areas of clouds

## Slide 7: Redundancy in M2M Topology
In some application domains such as a large scale environment monitoring system, the IoT devices can be scattered and decentralized.
These devices may require to interact with each other to exchange their local computation.
In order to increase the redundancy in such a scenario, researchers have suggested storing replicas of the local data and computation on the neighboring devices
Each device computes its own application, and also knows where its own local applications have been replicated. Furthermore, it monitors another device(s) through a heartbeat mechanism

## Slide 8: Graceful Degradation
In order to make the autonomous objects as well as the service platform of an IoT system survive for long, a graceful degradation (also known as fail-safe) capability should be built-into the components.
When an unexpected event occurs, a gracefully degradable system can remain partly operational, rather than failing completely. However, as the system designer, it is important to define what degradation means in a given application context.

## Slide 9: ERROR DETECTION (technique for addressing reliability)
Heartbeat
Watchdog
Exception Handling
Recovery Through Restart
Use of heartbeat and watchdog timers are traditional approaches to make the operational state visible to the outside world, which can help in detecting the failure of any node in a networked, real-time system.

## Slide 10: Watchdog
Timer Reset, Timer Countdown, Watchdog Timer Expiry, Watchdog Action are the flow of watchdog timer.
  This is a lightweight timer, which runs separately from the main process. The watchdog timer is initially set to a specific timeout value. As long as the software or system is running correctly, the software periodically resets or "feeds" the watchdog timer before it reaches zero(expire).
  If, for any reason, the software fails to reset the watchdog timer within the specified time interval, the timer reaches zero. The process is assumed to have a control flow error (the correct flow of control would have reset the timer).
In such a case, a hardware-implemented timer can generate an interrupt that can trigger a recovery routine. When the watchdog timer expires, it triggers a predefined action.
The recovery procedure can
  1. Restart the process or the system from its check pointed state
  2. Invoke an appropriate recovery routine

## Slide 11: Heartbeat
The term "heartbeat" generally refers to a signal or message sent between components to indicate their operational status or to confirm ongoing communication. The heartbeat mechanism helps ensure the health and proper functioning of components within a system
In this approach, a node in the network sends a message with a payload (ie, meaningful results, execution progress) to indicate that it is alive.
If the heartbeat signal is not received within the prescribed time, the monitoring component assumes that the application running on the node has failed.

## Slide 12: Exception Handling
The basic concept behind an error detection technique is that an application satisfies a set of properties for all correct executions of the application.
If the property is not satisfied for any run of the program due to a fault, exception occurs in the program.
Automatic Recovery Mechanisms are Implemented that enable automatic recovery from certain types of errors or faults.
It Reduces downtime and manual intervention by allowing devices to autonomously recover from common issues.

## Slide 13: Recovery Through Restart
Error detection, it is essential to implement a recovery mechanism for IoT components.
At a minimum, autonomous devices as well as network devices need to have a basic restart mechanism, which can be triggered by the watchdog timer, or by the service platform.
Recovery through restart is a simple and effective strategy, especially for transient or temporary issues. However, it may not be suitable for all scenarios, particularly in situations where continuous operation is critical.

## Slide 14: FAULT PREVENTION (technique for addressing reliability)
Fault prevention implies that faults are prevented from occurring on the runtime system
In traditional high availability systems, it is a common practice to detect failure possibility and remove a part of the system that can potentially fail
Another approach to prevent failures in high-availability system is to perform scheduled maintenance and timely software upgrades

## Slide 15
Failure Prediction: it is possible to implement a monitor that can watch for a failure, and can take a preventive action. These can be ensured at Program level, Process level and Infrastructure level
Improving Communication Reliability: In IoT application scenarios, the communication of machines and sensors without human intervention is a key requirement. To achieve this goal without failure, the reliability of the communication system that connects the sensors together plays a key role in the overall system reliability.
Improving Energy Efficiency : By the approach to optimize the energy consumption needs to be considered to prevent any failure due to the unavailability of the battery power
FAULT PREVENTION (technique for addressing reliability)